Kyungmook Park

CS 6097 Wireless and Mobile Networking
Homework No. 6 dated Wednesday October 8, 2014

P9.6.	Assume that you just got out of an airplane and you switched on your cell phone. If the closest BS is located at a distance of 5 km, what are the minimum and the maximum delay before a contact is established between your cell phone and the nearest BS, given that the BS transmits beacon signals every one second?

Signal travel time = Distance / Speed of Light = 5000m / 299792458 = 0.0167 ms.
Minimum delay occurs when I switch on my phone just before the BS transmits the signal. 0.0167 ms is the minimum delay.
Maximum delay occurs when I switch on my phone right after the BS transmits the signal. 1000.0167 ms is the maximum delay.

P9.8.	What is the use of “attachment points” from one network to another network? Explain their significance in wireless network routing?

Attachment point serves as a point of hand-off between the Foreign Agent (FA) and the Home Agent (HA). As the MS moves from the HA to the FA, the packets must be continuously sent in order to prevent losing data between hand-off.

P10.3.	Look at your favorite Web site and find the difference between interior and exterior routing protocols.

Reddit.com has multiple subreddits (or forum threads) that allow users to navigate within the web site (interior routing protocol). Also, it contains links to other web sites such as Imgur and BuzzFeed (exterior routing protocol).

P10.8.	What are the disadvantages of using wireline TCP over wireless networks?

Some of the disadvantages of using wireline TCP include frequent window reduction due and timeout due to packet loss because congestion can be present at various nodes in the network.